## Slide 1: RepCut: Superlinear Parallel RTL Simulation with Replication-Aided Partitioning
By Haoyuan Wang, Scott Beamer
Presenter: Boyang Zhang, Department of ECE, UW Madison
bzhang523@wisc.edu

## Slide 2: About me
Education
  BS in School of Electronic and Information, South China University of Technology, China, 2020.
  MS in Department of ECE, Rutgers University, 2021.
  Second-year PhD student (supervisor: Prof. Tsung-Wei Huang).
Current research
  Incremental task graph partitioning.
  A paper[1] of task graph partitioning was accepted to DAC’24.
  I am submitting a paper to ICCAD’24.
[1] Boyang Zhang, Dian-Lun Lin, Che Chang, Cheng-Hsiang Chiu, Bojue Wang, Wan Luan Lee, Chih-Chun Chang, Donghao Fang, and Tsung-Wei Huang, "G-PASTA: GPU Accelerated Partitioning Algorithm for Static Timing Analysis," ACM/IEEE Design Automation Conference (DAC), San Francisco, CA, 2024

## Slide 3: Outline
Introduction to RTL simulation
  What is RTL simulation?
  Why partitioning?
  Partitioning challenges?
Introduction to RepCut
  Partitioning algorithm walkthrough
  Scheduling the partitions
  Experimental results
Current research
  Limitations of RepCut partitioning
  PASTA partitioning

## Slide 4: Introduction to RTL simulation

## Slide 5: What is RTL simulation?
A process to simulate the behaviors of a Register Transfer Level(RTL) design to verify its functionality.
Event-driven(more accurate) or full-cycle(less time-consuming).
Full-cycle simulator: Verilator[2], ESSENT[3](unoptimized).
[2] https://github.com/verilator/verilator
[3] https://github.com/ucsc-vama/essent
Notes: So, what is RTL simulation?
It is a process to simulate the behaviors of a Register Transfer Level design to verify the design’s functionality and correctness
RTL simulator can be mainly classified as 2 types, event-driven RTL simulator and full-cycle RTL simulator.
An event-driven simulator takes each change of the input stimulus as an event and propagate this value changes through the circuit.
A full-cycle simulator is oblivious to the changes of input stimulus within one cycle and only stimulates the design once per cycle.
So in a word, an event-driven simulator gives more accurate simulation results but when it comes to very large circuit design, full cycle RTL simulator is much faster.
In this paper, we focus on full-cycle RTL simulator and there are 2 full-cycle RTL simulators that are evaluated in this paper, Verilator, and ESSENT.
More specifically, the partitioning method introduced by RepCut is operated in an unoptimized version of ESSENT to demonstrate its effectiveness verses the baseline partitioning
method in Verilator, which we will talk a bit more in experimental results.

## Slide 6: Why partitioning?
RTL simulation is very time-consuming for large designs.
RTL simulation in parallel?
Represent the design as a task dependency graph(TDG).
Node: the simulation task of a logic gate/register.
Edge: the connection between logic gates/registers.
Too fine-grained.
Partition the TDG.
Notes: So, this paper talks about partitioning in RTL simulation.
First, we need to answer a question, why do we need partitioning in RTL simulations.
Well as I mentioned in the first slide, RTL simulation is very time-consuming when it comes to large designs even for a full-cycle simulator.
For a very large design that contains millions or billions of gates, RTL simulation can be bottleneck in the whole circuit design process.
So how to speedup this simulation process, well naturally we will think about maybe we can do it in parallel.
A typical first step to do RTL simulation in parallel is to represent the hardware design as a TDG, which is a task dependency graph.
TDG is essentially a dependency acyclic graph.
For TDGs in RTL simulation, each node represents a simulation task of a register or a logic gate that we want to test in the design.
Each edge represents the connections among these logic gates and registers.
With TDGs, we can distribute each simulation task to CPU/GPU threads to do them in parallel.
But, as I said, the circuits can contain billions of gates, and such fine-grained distribution of tasks is just too overwhelming to CPU or even GPU!
To solve this issue, we can coarsen the TDG by partitioning it.
Partitioning a TDG here is to cluster multiple gates or registers into one partition, or one task.
After this, we can distribute the partitions to either CPU/GPU threads to achieve RTL simulations in parallel.

## Slide 7: Partitioning challenges?
Balanced and minimal inter-communication
Notes: Now, what are the challenges for partitioning such a TDG in RTL simulations?

## Slide 8
Chart: 
| Category 1 | Category 2 | Category 3
Series 1 | 4.3 | 2.5 | 3.5
Series 2 | 2.4 | 4.4 | 1.8
Series 3 | 2 | 2 | 3
Series 4 | 2.1 | 3 | 2.9
Series 5 | 2.5 | 3.4 | 2.4
Series 6 | 3.4 | 2.7 | 3

## Slide 9
Chart: 
| Category 1
Series 1 | 4.3
Series 2 | 2.4
Series 3 | 2
Series 4 | 2.1
Series 5 | 2.5
Series 6 | 3.4

## Slide 10
Chart: 
| Category 1
Series 1 | -1.5
Series 2 | 2.4
Series 3 | 2
Series 4 | 2.1
Series 5 | 2.5
Series 6 | 3.4

## Slide 11
Chart: Chart Title
| Category 1 | Category 2 | Category 3 | Category 4 | Category 5 | Category 6
Series 1 | 4.3 | 2.5 | 3.5 | 4.5 | 5 | 1.2
Series 2 | 2.4 | 4.4 | 1.8 | 2.8
Series 3 | 2 | 2 | 3 | 5
Series 4 | 2.1 | 3 | 2.9 | 4.2
Series 5 | 2.5 | 3.4 | 2.4 | 3.2

## Slide 12
Chart: Chart Title
| Category 1 | Category 2 | Category 3 | Category 4 | Category 5 | Category 6
Series 1 | 4.3 | 2.5 | 3.5 | 4.5 | 5 | 1.2
Series 2 | 2.4 | 4.4 | 1.8 | 2.8
Series 3 | 2 | 2 | 3 | 5
Series 4 | 2.1 | 3 | 2.9 | 4.2
Series 5 | 2.5 | 3.4 | 2.4 | 3.2